## Slide 1: Early Detection of Turbofan Failure
Predicting failure before it happens

## Slide 2: Data & Scope
The data provided for 100 engines consists of the following columns:
  3 settings,
  21 sensors,
  Engine cycles w.r.t when it was collected.
Out of these columns:
  Setting 3 & sensors 1, 5, 9, 10, 14, 16, 18 & 19 did not provide any useful insights.
  Engine cycles was used to determine the remaining cycles left.
Remaining cycles (RC) is what the model will predict:
  Predicting the RC will be robust for your future use case;
  To predict if the engine will fail within the next 15 cycles.

## Slide 3: Metric & Evaluation
The model will base itself on a metric & attempt to minimize its error through its training.
  The chosen metric is the Mean Squared Error (MSE) for model training;
  this measures the average of the squares of the errors.
  A higher MSE interprets to be a poor model.
  For ease of explanation, we will use the Root Mean Squared Error (RMSE), which is the square root of the MSE.
As a baseline, we achieved an RMSE of 40.48.
The final model achieved an RMSE of 16.76. (58.5% improvement from baseline)
  This is based on a 2-layer (Long Short-Term Memory) LSTM model

## Slide 4: What Does This Mean?
Since the model predicts the remaining cycles left, and a model is never 100% accurate;
  We propose a buffer of 4 engine cycles to obtain a 96% confidence that an engine failure will not fail in less than 15 cycle once the fault is detected.
  You may adjust this buffer if the confidence obtained is not acceptable.